## Slide 1: VATRA HPP
ON THE RIVER JEJORA

## Slide 2: Site Location
VATRA HPP
 | X | Y
Head unit on the river Jejora | 384840 | 4706372
Powerhouse Location | 380904 | 4708345

## Slide 3: Brief Description of Site
The project envisages the optimal use of the energy potential the River Jejora between the absolute elevations ∇1177.0 - 992.0 m.a.s.l., the tributary of the River Chanchakhi in Oni municipality, Racha region, Georgia
The project envisages the construction of 16.67 MW hydro power plant, which will generate 84.15 GWh electricity annually.

## Slide 4: Key Technical Parameters
Name | Dimension | Data
Normal supply level | m a.s.l | 1177.0
Type of regulation | _ | run-of the river
HPP scheme | _ | diversion
Average multi-annual water discharge | m3/sec | 8.75
Rated water discharge | m3/sec | 11.0
Sanitary flow | m3/sec | 0.88
Number of units | unit | 2
Turbine type | _ | “FRANCIS”
Rated water discharge for the turbine | m3/sec | 5.50
Rated (net) head | m | 175.03
Nominal capacity of a plant | MW | 8.33
Installed capacity | MW | 16.67
Guaranteed winter capacity (P=50%) | MW | 3.33

## Slide 5: Power Generation
Average annual Generation | GWh | 84.15
Generation at 10% provision | GWh | 97.55
Generation at 50% provision | GWh | 82.84
Generation at 90% provision | GWh | 63.68
Installed capacity usage ratio (ICUR) | % | 57.64

## Slide 6: Technical Design

## Slide 7: Technical Design

## Slide 8: Connection to the Grid

## Slide 9: BoQ & Cost Estimates
Structures | Name of works to be performed | Dimension | Quantity | Unit rate in USD | Total price
Head work structure: dam | Earth work | m3 | 8,540.00 | $4.00 | $34,160.00
 | Backfill | m3 | 1,240.00 | $4.00 | $4,960.00
 | Quality backfill | m3 | 8,000.00 | $8.00 | $64,000.00
 | Concrete/R/C | m3 | 3,970.00 | $120.00 | $476,400.00
 | Construction steel | t | 51.90 | $520.00 | $26,988.00
 | Metal structure | t | 30.00 | $2,500.00 | $75,000.00
Diversion: tunnel, head pool, penstock | Earth work | m3 | 100,691.20 | $30.00 | $3,020,736.00
 | Backfill | m3 | 8,653.80 | $4.00 | $34,615.20
 | Concrete/R/C | m3 | 18,359.06 | $120.00 | $2,203,087.20
 | Construction steel | m3 | 552.30 | $520.00 | $287,196.00
 | Metal structure | t | 4.00 | $2,500.00 | $10,000.00
 | Metal pipeline | t | 788.38 | $880.00 | $693,770.44
Powerhouse | Earth work | m3 | 2,400.00 | $4.00 | $9,600.00
 | Backfill | m3 | 1,000.00 | $4.00 | $4,000.00
 | Concrete/R/C | m3 | 1,100.00 | $120.00 | $132,000.00
 | Construction steel | m3 | 55.00 | $520.00 | $28,600.00
 | Metal structure | t | 8.00 | $2,500.00 | $20,000.00
 | E&M | t | 16.67 | $350,000.00 | $5,834,500.00
Outlet channel | Earth work | m3 | 1,305.85 | $4.00 | $5,223.40
 | Backfill | m3 | 483.80 | $4.00 | $1,935.20
 | Concrete/R/C | m3 | 162.36 | $120.00 | $19,483.20
 | Construction steel | m3 | 6.49 | $520.00 | $3,377.09
Infrastructure | New road, 4.0 m wide | km | 0.50 | $50,000.00 | $25,000.00
Transmission line 35 kV | 35 kv | km | 3.50 | $80,000.00 | $280,000.00
Total construction |  |  |  |  | $13,294,631.73
Contingencies (20%) | USD |  |  |  | $2,658,926.35
Technical design works, management and supervision (7%) | USD |  |  |  | $1,116,749.07
Total including VAT | USD |  |  |  | $17,070,307.14

## Slide 10: Financial Analysis
Investment (USD Mln. Excluding VAT) | 14.47 | 
Duration of construction (years) | 3 | 
Annual Generation | GWh | MWh
Capacity | 84.2 | 84,150.0
Installed capacity | 16.7 | 
Financial data in USD "000000" | 1,000,000.0 | 
Currency | USD | 
Project year | 2020 | 
Taxes |  | 
Profit tax | 15% | 
Property tax | 1% | 
VAT | 18% | 
Prices USD/kWh |  | 
4 month (Summer price) | 0.040 | 
Average annual Price growth rate | 0.000 | 
8 month (Winter price) | 0.055 | 
Average annual Price growth rate | 0.0% | 
Operating cost site |  | 
O&M | 2.00% | 
Capital Expances | 1.00% | 
Technical losses and own consumption | 1.00% | 
Sales distribution |  | 
4 month (Summer generation) | 51% | 
8 month (Winter generation) | 49% | 
Capital structure |  | USD "000000"
Total investment | 100% | 14.47
Debt | 70% | 10.13
Equity | 30% | 4.34
Debt |  | 
Amount | 10.13 | 
Interest rate | 10% | 
Maturity (years) | 10 | 
Discount rate |  | 
Cost of equity | 12% | 
Cost of debt | 10% | 
WACC | 9.55% | 

## Slide 11: Financial Analysis
Results | 
Project NPV | 12.36
Equity NPV | 7.18
Project IRR | 18.3%
Equity IRR | 22.3%
Payback (years including construction period) | 8